## Slide 1
BIRLA INSTITUTE OF TECHNOLOGY & SCIENCE, PILANI
WORK INTEGRATED LEARNING PROGRAMMES (WILP) DIVISION - COURSE NO. ESZG628T: DISSERTATION
DISSERTATION OUTLINE PRESENTATION
POST-QUANTUM FIRMWARE AUTHENTICATION:
DESIGN AND IMPLEMENTATION OF A QUANTUM-RESISTANT SECURE BOOT MECHANISM
Student Name: Kiruthik Prakash J | BITS ID: 2024HT01586
Degree Program: M.Tech in Embedded Systems | Research Area: Embedded Systems
Employing Organization: Qualcomm India Private Limited, Hyderabad
Email: 2024h01586@wilp.bits-pilani.ac.in | Academic Year: Second Semester 2025-2026 (August 2026)
SUPERVISOR
Deepak Kumar (B.Tech ECE)
Senior Lead Software Engineer
Qualcomm India Private Limited, Hyderabad
Email: kudee@qti.qualcomm.com | Phone: +91 8223050025
ADDITIONAL EXAMINER
Divyasree Chilukoti (M.Tech - InfoSec)
Senior Engineer
Qualcomm India Private Limited, Hyderabad
Email: dchiluko@qti.qualcomm.com | Phone: +91 9398527351
Birla Institute of Technology & Science, Pilani (Vidya Vihar, Pilani, Rajasthan - 333031) - August 2026
Notes: Estimated Time: 1 min 00 sec | Cumulative: 1:00
Spoken Dialogue: Welcome to my M.Tech Dissertation Outline presentation for Course ESZG628T: Dissertation...

## Slide 2
1. BROAD AREA OF WORK
Broad Area of Work: Overview & Focus Areas
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 2 / 12
RESEARCH DOMAIN & KEY CONTRIBUTIONS
- Exploring post-quantum cryptography in embedded firmware security.
- Developing quantum-resistant secure boot mechanisms for microcontrollers.
- Establishing tamper-evident chain of trust using PQC.
- Executing zero-malloc cryptographic validations within static SRAM.
- Seamlessly integrating PQC into real-world bootloaders.
HETEROGENEOUS TARGET SYSTEM TAXONOMY
Tier 1: IoT & Microcontrollers
PRIMARY MCU TARGET
Target Bootloader: MCUboot (Zephyr / FreeRTOS)
Hardware Target: ARM Cortex-M4 (32-bit Bare-Metal)
Memory Ceiling: Strict Zero-Malloc, SRAM < 4 KB
Tier 2: Embedded Linux Gateways
SECONDARY TARGET
Target Bootloader: Das U-Boot (FIT Container Image)
Hardware Target: 64-bit RISC-V (QEMU virt)
Memory Ceiling: Static SRAM Buffers, Zero Heap
Tier 3: Enterprise & Edge Servers
ENTERPRISE TARGET
Target Bootloader: EDKII / UEFI (SecurityPkg)
Hardware Target: Multi-Core ARM Cortex-A57
Memory Ceiling: Pre-EFI Initialization (PEI) Stage
UNIFIED POST-QUANTUM C99 ENGINE
Single Portable Verification Core across all 3 Systems
NIST ML-DSA-44 | SPHINCS+ | Stateful LMS
Notes: Estimated Time: 1 min 15 sec | Cumulative: 2:15
Spoken Dialogue: Section 1 defines the Broad Area of Work...

## Slide 3
2. BACKGROUND: THREAT MODEL
Background: The Impending Quantum Threat
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 3 / 12
POST-QUANTUM CRYPTOGRAPHIC THREAT
- Secure boot establishes tamper-evident hardware Root-of-Trust.
- Classical RSA and ECDSA protect firmware today.
- Shor's algorithm solves factorisation in polynomial time.
- Quantum computers render classical digital signatures obsolete.
- Exposes bare-metal systems to unauthorized firmware execution.
CRYPTOGRAPHIC HARDNESS & QUANTUM STATUS
RSA-2048 / RSA-3072
BROKEN BY QUANTUM
Underlying Hardness: Integer Factorization Problem
Classical: Sub-exponential L_N[1/3]
Quantum Complexity: Shor O((log N)^3) Polynomial Time
ECDSA P-256 (ECC)
BROKEN BY QUANTUM
Underlying Hardness: Elliptic Curve Discrete Log (ECDLP)
Classical: Exponential O(sqrt(p))
Quantum Complexity: Shor O((log N)^3) Polynomial Time
ML-DSA-44 (Dilithium)
QUANTUM-SAFE (FIPS 204)
Underlying Hardness: Module Learning With Errors (M-LWE)
Classical: Lattice Shortest Vector Problem (SVP)
Quantum Complexity: Exponential (Lattice sieving/BKZ)
SPHINCS+ / LMS
QUANTUM-SAFE (FIPS 205)
Underlying Hardness: Hash Function Preimage Resistance
Classical: Exhaustive preimage search O(2^n)
Quantum Complexity: Grover quadratic bound O(2^(n/2))
Notes: Estimated Time: 1 min 30 sec | Cumulative: 3:45
Spoken Dialogue: Section 2 details the background and threat landscape...

## Slide 4
2. BACKGROUND: SYSTEMS CONSTRAINTS
Background: Systems Engineering Challenges
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 4 / 12
BARE-METAL FIRMWARE CONSTRAINTS
- Integrating post-quantum signatures presents severe engineering challenges.
- Bootloaders mandate zero dynamic memory allocation calls.
- Cryptographic verification runs within static SRAM buffers.
- Automotive and industrial systems demand low latency.
- Bridges theoretical standards and production firmware implementations.
EMBEDDED PQC RESOURCE BUDGET COMPARISON
ECDSA P-256 (Classical Baseline)
CLASSICAL BASELINE
Signature Size: 64 Bytes | Public Key: 64 Bytes
Stack RAM Need: < 1.0 KB | Latency: ~2 to 4 ms
Assessment: Minimal memory; fatally vulnerable to quantum
LMS (RFC 8554 Stateful Hash)
FASTEST PQC VERIFY
Signature Size: ~2.5 KB | Public Key: 56 Bytes
Stack RAM Need: < 2.0 KB | Latency: < 3.5 ms
Assessment: Ultra-fast verification; ideal for Stage-0 Mask ROM
ML-DSA-44 (NIST FIPS 204)
OPTIMAL EMBEDDED FIT
Signature Size: 2,420 Bytes | Public Key: 1,312 Bytes
Stack RAM Need: ~3.5 KB | Latency: ~8 to 15 ms
Assessment: Optimal general-purpose fit for MCUboot & U-Boot
SPHINCS+-SHA2-128s (FIPS 205)
STACK INTENSIVE
Signature Size: 7,856 Bytes | Public Key: 32 Bytes
Stack RAM Need: > 4.5 KB | Latency: ~40 to 110 ms
Assessment: Conservative stateless hash; high stack for MCUs
Notes: Estimated Time: 1 min 30 sec | Cumulative: 5:15
Spoken Dialogue: Continuing with Section 2, integrating post-quantum signatures...

## Slide 5
3. OBJECTIVES
Objectives of the Dissertation
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 5 / 12
DISSERTATION RESEARCH OBJECTIVES
- Design zero-malloc static-stack C post-quantum verification library.
- Verify NIST ML-DSA-44, SPHINCS+, and LMS algorithms.
- Integrate PQC parsers across diverse bootloader frameworks.
- Extend firmware signing tools with custom headers.
- Establish multi-architecture validation setups using QEMU emulation.
SYSTEMATIC OBJECTIVES EXECUTION PIPELINE
1. Zero-Malloc C99 Verification Library
ML-DSA-44 / SPHINCS+ / LMS (< 4 KB Static SRAM)
2. Bootloader Architecture Integration
MCUboot (ARM-M4) | U-Boot FIT (RISC-V) | UEFI (Cortex-A57)
3. Firmware Signing & Container Toolchain
Custom PQC TLV Headers (0x80-0x88) and Object Identifiers
4. QEMU Emulation & Empirical Validation
GDB Memory Profiling, Fault Injection, 100% Tamper Rejection
Notes: Estimated Time: 1 min 30 sec | Cumulative: 6:45
Spoken Dialogue: Section 3 articulates the core Objectives...

## Slide 6
4. SCOPE: PHASE 1
Scope: Phase 1 - Crypto Engine & Container Design
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 6 / 12
PHASE 1 CORE DELIVERABLES
- Define memory bounds for bare-metal verification environments.
- Select NIST-standardized PQC schemes for constrained systems.
- Design standalone zero-malloc C signature verification library.
- Execute validation strictly within bounded static SRAM.
- Define metadata container formats and custom headers.
CRYPTO ENGINE & CONTAINER DESIGN PIPELINE
1. Algorithm Selection and Security Bounds
ML-DSA-44 (Lattice) | SPHINCS+ | LMS
2. Zero-Malloc C99 Verification Library
Deterministic Static-Stack Memory Architecture
3. Static SRAM Verification Budget
Memory Ceiling Mathematically Bounded < 4 KB
4. Metadata Containers and Headers
Custom TLV Schema and PKCS#7 OID Structures
5. Extended Host Signing Utilities
Automated CI/CD Keygen and Container Encapsulation
Notes: Estimated Time: 1 min 15 sec | Cumulative: 8:00
Spoken Dialogue: Section 4 establishes the formal Scope of Work...

## Slide 7
4. SCOPE: PHASE 2
Scope: Phase 2 - Multi-Target Integration & Trust Chain
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 7 / 12
PHASE 2 TARGET INTEGRATION SCOPE
- IoT targets: Integrate PQC into lightweight MCUboot.
- Embedded Linux: Extend Flattened Image Tree verification.
- Enterprise systems: Incorporate PQC into UEFI SecurityPkg.
- Configure QEMU system emulation for multi-architecture targets.
- Support ARM Cortex-M4, RISC-V 64, and Cortex-A57.
SECURE BOOT CHAIN OF TRUST ARCHITECTURE
Immutable Hardware Root of Trust
Write-Protected Mask ROM & Hardware OTP Fuses
Stage 0: Primary Bootloader (MCUboot)
ARM Cortex-M4 (32-bit) | LMS / ML-DSA-44
Stage 1: Secondary Bootloader (U-Boot FIT)
64-bit RISC-V Target | ML-DSA-44 Signature
Stage 2: Enterprise OS Loader (UEFI)
Multi-Core ARM Cortex-A57 | SecurityPkg PQC
AUTHENTICATED OPERATING SYSTEM
Fully Verified, Tamper-Evident Kernel Execution
Notes: Estimated Time: 1 min 30 sec | Cumulative: 9:30
Spoken Dialogue: Continuing with Section 4, Phase 2 covers Multi-Target Integration...

## Slide 8
4. SCOPE: PHASE 2 DEEP DIVE
Scope: Phase 2 - MCUboot Implementation Architecture
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 8 / 12
MCUBOOT ARCHITECTURAL WORKFLOW
- Deep dive into MCUboot IoT firmware authentication.
- Hardware RoT keys embedded in static flash.
- Custom PQC TLV headers encapsulate signature payloads.
- SHA-256 and SHA-512 compute immutable firmware digest.
- Verifies signature within bounded static stack memory.
FLASH STREAMING VERIFICATION PIPELINE
Flash TLV Trailer Parser
Parse Tag, Length, Value (PQC Sig: 0x80 - 0x88)
Digest Commitment Engine
Incremental SHA-256 Hash over Image Slot
Zero-Heap PQC Verifier
Verify Signature using OTP Root Public Key
Cryptographic Verification Gate
SIGNATURE VALID
Set image status OK; jump to Cortex-M4 reset vector
TAMPER / MISMATCH
Trigger security fault; fail-secure immediate halt
Operates entirely in-place. If any bit in the header, image, or signature is flipped, MCUboot halts deterministically.
Notes: Estimated Time: 1 min 30 sec | Cumulative: 11:00
Spoken Dialogue: Continuing with Phase 2, Slide 8 presents our deep dive into MCUboot...

## Slide 9
4. SCOPE: PHASE 3
Scope: Phase 3 - Validation & Security Benchmarking
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 9 / 12
PHASE 3 EMPIRICAL VALIDATION
- Execute automated full boot sequences in QEMU.
- Use GDB to enforce static memory limits.
- Verify total absence of dynamic heap allocations.
- Test fault-injection with bit-flipped signatures and headers.
- Benchmark PQC implementations against classical RSA baselines.
AUTOMATED TESTBENCH & PROFILING HARNESS
Automated Test Runner & Mutator
Python E2E Test Suite via Multi-Target QEMU
1. QEMU Multi-Arch Emulation
ARM Cortex-M4 | RISC-V 64 | Cortex-A57
2. GDB Stack Memory Profiling
Enforcing Static Ceiling (< 4 KB) & Zero Dynamic Heap
3. Bit-Flip Fault Injection
Simulated Tampering: Signatures, TLVs, Keys
100% TAMPER REJECTION & BENCHMARKS
Signature Overhead, ROM/RAM Footprint, Boot Latency
Notes: Estimated Time: 1 min 15 sec | Cumulative: 12:15
Spoken Dialogue: Phase 3 of the Scope covers Validation and Security Benchmarking...

## Slide 10
5. PLAN OF WORK
Plan of Work: Five-Phase Implementation Roadmap
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 10 / 12
ACADEMIC TIMELINE: SECOND SEMESTER 2025-2026 (JULY 2026 --> DECEMBER 2026)
PHASE 1
Dissertation
Outline
25 Jul - 8 Aug 2026
- Literature review on NIST FIPS 204, FIPS 205, and RFC 8554.
- Zero-malloc & static-RAM constraint model (< 4 KB).
- Root of Trust hardware security specifications.
- Formal Dissertation Outline report submission & review.
PHASE 2
Design &
Development
9 Aug - 31 Oct 2026
- Zero-malloc C99 PQC verification library implementation.
- Firmware metadata container & custom TLV / OID formats.
- Bootloader integration: MCUboot, U-Boot FIT, and UEFI.
- Host image signing utilities & test vector packaging.
PHASE 3
Software
Testing
1 Nov - 19 Nov 2026
- Automated Python test harness via multi-target QEMU.
- ARM Cortex-M4, 64-bit RISC-V, and Cortex-A57 validation.
- GDB stack profiling to mathematically enforce zero-heap.
- Fault-injection testing: 100% bit-flip tamper rejection.
PHASE 4
Dissertation
Review
20 Nov - 30 Nov 2026
- Draft dissertation submission to Qualcomm review committee.
- Formal evaluation by Deepak Kumar & Divyasree Chilukoti.
- Benchmark analysis vs. classical RSA and ECDSA baselines.
- Review feedback incorporation and pre-defense audit.
PHASE 5
Final
Submission
1 Dec - 8 Dec 2026
- Final dissertation report binding and documentation.
- Formal submission to BITS Pilani WILP Division.
- Final oral dissertation examination and defense.
- Research artifact publication and code archival.
Notes: Estimated Time: 1 min 15 sec | Cumulative: 13:30 Spoken Dialogue: 'Section 5 outlines our official Plan of Work and milestone timeline across the second semester of academic year 2025-2026. As shown in our enlarged chronological roadmap, the project executes across five structured phases: Phase 1, from 25 July to 8 August: We completed the literature review across NIST FIPS 204, FIPS 205, and RFC 8554, established zero-malloc and static-SRAM constraint models under 4 KB, and formalized our Dissertation Outline. Phase 2, from 9 August to 31 October: We execute core Design and Development, implementing the zero-malloc C99 verification library for ML-DSA-44, SPHINCS+, and LMS, integrating hooks into MCUboot, U-Boot FIT, and UEFI SecurityPkg, and extending host signing tools. Phase 3, from 1 November to 19 November: We conduct Software Testing, launching automated Python test suites in QEMU across ARM Cortex-M4, 64-bit RISC-V, and Cortex-A57 targets, profiling stack usage in GDB, and verifying 100% tamper rejection under bit-flip fault injection. Phase 4, from 20 November to 30 November: We submit the draft dissertation for formal evaluation by Supervisor Mr. Deepak Kumar and Additional Examiner Ms. Divyasree Chilukoti at Qualcomm. Phase 5, from 1 December to 8 December: We incorporate final feedback, finalize the dissertation report, and complete our oral defense examination.'

## Slide 11
6. LITERATURE REFERENCES
Literature References: Authoritative Research Foundations
BITS Pilani (WILP) | ESZG628T Dissertation Outline | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 11 / 12
PQC STANDARDS & THEORETICAL FOUNDATIONS
[1] NIST FIPS 204 (August 2024)
National Institute of Standards and Technology (NIST), "Module-Lattice-Based Digital Signature Standard (ML-DSA)", Federal Information Processing Standards Publication (FIPS) 204, U.S. Department of Commerce. https://doi.org/10.6028/NIST.FIPS.204
[2] NIST FIPS 205 (August 2024)
National Institute of Standards and Technology (NIST), "Stateless Hash-Based Digital Signature Standard (SLH-DSA / SPHINCS+)", Federal Information Processing Standards Publication (FIPS) 205, U.S. Department of Commerce. https://doi.org/10.6028/NIST.FIPS.205
[3] IETF RFC 8554 (April 2019)
D. McGrew, M. Curcio, and S. Fluhrer, "Leighton-Micali Hash-Based Signatures (LMS)", Internet Engineering Task Force (IETF) Request for Comments (RFC) 8554. https://doi.org/10.17487/RFC8554
[4] IETF RFC 8708 (February 2020)
R. Housley, "Use of the Leighton-Micali Signature (LMS) Algorithm in CMS", Internet Engineering Task Force (IETF) Request for Comments (RFC) 8708. https://doi.org/10.17487/RFC8708
[5] IEEE FOCS 1994 (Foundational)
Peter W. Shor, "Algorithms for Quantum Computation: Discrete Logarithms and Factoring", Proc. 35th Annual IEEE Symposium on Foundations of Computer Science, pp. 124-134. https://doi.org/10.1109/SFCS.1994.365700
POST-QUANTUM SCHEMES & BOOTLOADER SPECS
[6] NIST PQC Submission (2019)
D. J. Bernstein, A. Huelsing, S. Koelbl, R. Niederhagen, A. Rijneveld, P. Schwabe, "SPHINCS+: Stateless Hash-Based Signatures Specification (ed. 2.1)", NIST Post-Quantum Cryptography Standardization Process. https://sphincs.org
[7] UEFI Specification 2.10 (2024)
Unified Extensible Firmware Interface (UEFI) Forum, "Unified Extensible Firmware Interface Specification, Version 2.10", Section 32: Secure Boot, Authentication Variables & PE/COFF Signature Verification. https://uefi.org
[8] MCUboot Specification (2024)
MCUboot Project Contributors, "MCUboot: Secure Bootloader for 32-bit Microcontrollers", Open Source Firmware Specification, Trailer TLV Format & Image Signing Architecture. https://github.com/mcu-tools/mcuboot
[9] Das U-Boot Architecture (2024)
DENX Software Engineering, "The Universal Boot Loader: Flattened Image Tree (FIT) Architecture", FIT Container Image Cryptographic Verification Architecture & Device Tree Signature Nodes. https://source.denx.de/u-boot/u-boot
Notes: Estimated Time: 1 min 15 sec | Cumulative: 14:45 Spoken Dialogue: 'Section 6 establishes the authoritative literature references that ground our dissertation research. On the left panel, we highlight the governing cryptographic standards and foundational mathematical theory: First, NIST FIPS 204 published in August 2024, standardizing Module-Lattice Digital Signatures (ML-DSA). Second, NIST FIPS 205, standardizing Stateless Hash-Based Digital Signatures (SLH-DSA / SPHINCS+). Third, IETF RFC 8554 and RFC 8708 by McGrew, Curcio, Fluhrer, and Housley, establishing Leighton-Micali Signatures and their integration into Cryptographic Message Syntax. Fourth, Peter Shorâ€™s seminal 1994 IEEE FOCS paper proving polynomial-time quantum attacks against integer factoring and discrete logarithms. On the right panel, we cite the open-source cryptographic scheme submissions and production bootloader specifications: Fifth, the SPHINCS+ submission specification by Bernstein, HÃ¼lsing, and co-authors. Sixth, the official UEFI Specification Version 2.10 governing secure boot architectures. Seventh, the MCUboot secure bootloader specification for 32-bit microcontrollers. And eighth, the Das U-Boot Flattened Image Tree verification architecture by DENX Software Engineering. These authoritative sources form the theoretical and architectural backbone of our zero-malloc implementation.'

## Slide 12
ESZG628T: DISSERTATION OUTLINE DEFENSE
Thank You
Questions & Technical Discussion
POST-QUANTUM FIRMWARE AUTHENTICATION: DESIGN AND IMPLEMENTATION OF A QUANTUM-RESISTANT SECURE BOOT MECHANISM
CANDIDATE
Kiruthik Prakash J
BITS ID: 2024HT01586
M.Tech in Embedded Systems
Qualcomm India Private Limited
2024h01586@wilp.bits-pilani.ac.in
SUPERVISOR
Deepak Kumar
Senior Lead Software Engineer
Qualcomm India Private Limited
Hyderabad, Telangana
kudee@qti.qualcomm.com
ADDITIONAL EXAMINER
Divyasree Chilukoti
Senior Engineer
Qualcomm India Private Limited
Hyderabad, Telangana
dchiluko@qti.qualcomm.com
Birla Institute of Technology & Science, Pilani - Work Integrated Learning Programmes (WILP) Division
Second Semester 2025-2026 | Pilani, Rajasthan - 333031 | Open for Questions, Evaluation & Discussion
BITS Pilani (WILP) | ESZG628T Dissertation Outline Defense | Kiruthik Prakash J (2024HT01586) | Qualcomm India
Slide 12 / 12
Notes: Estimated Time: 1 min 30 sec | Cumulative: 16:15 Spoken Dialogue: 'Esteemed supervisor Mr. Deepak Kumar, additional examiner Ms. Divyasree Chilukoti, and respected faculty members of BITS Pilani: This concludes my formal presentation of the dissertation outline for "POST-QUANTUM FIRMWARE AUTHENTICATION: DESIGN AND IMPLEMENTATION OF A QUANTUM-RESISTANT SECURE BOOT MECHANISM". I express my deepest gratitude to my supervisor, Mr. Deepak Kumar, for his continued mentorship and technical guidance, to Ms. Divyasree Chilukoti for her constructive feedback, and to the faculty of the Work Integrated Learning Programmes Division at BITS Pilani for their academic support. I am now eager to receive your questions, insights, and guidance to steer our development across the upcoming semester. Thank you very much. The floor is now open for questions and discussion.'